## Slide 1
M.I.N.E.R.S. SYSTEM ARCHITECTURE
Mobile Intelligent Navigation and Emergency Rescue System | SIH 2026 (PS ID: 26039)
1. SENSE
Multi-Modal Sensors
2. COMPUTE
Edge Processing
3. UNDERSTAND
Perception & Fusion
4. ASSESS
Risk & Governor
5. DECIDE
Autonomous Mission
6. ACT
4WD Rugged Response
7. RESCUE
Surface Dashboard
1. SENSING LAYER
“Sense the Mine”
• 360° 2D LiDAR
2D Tunnel Contour & Obstacle Boundary
• Stereo RGB-D Camera
Dense Depth Estimation & Video Feed
• Thermal Camera
Infrared Heat Signature & Survivor Spot
• Multi-Gas Sensor Array
CH4, CO, CO2, O2, Flammable/Toxic Gases
• Environmental Sensors
Temperature, Humidity, Airflow, Dust
• Ultrasonic Array
Blind-Spot & Water Puddle Redundancy
• IMU + Wheel Encoders
Dead Reckoning & Odometry Tracking
2. EDGE COMPUTE
“Process Locally”
• Raspberry Pi 5 (8GB)
System Orchestration, ROS2 Core, Logging
• Raspberry Pi AI HAT+
26 TOPS NPU: Vision & Deep Learning
• Arduino Mega 2560
Hard Real-Time Motor & Sensor Polling
• Power Distribution
12V/24V Regulated Power Rail & BMS
• Hardware Watchdog
Fail-Safe Heartbeat & Relay Dropper
3. AI PERCEPTION
“Understand Mine”
• 2D LiDAR SLAM
Real-Time 2D Grid Mapping (RTAB/Fast-LIO)
• Stereo Depth Fusion
Debris Clearance & Passage Traversability
• Thermal + RGB Fusion
Trapped Miner Detection in Dense Smoke
• Edge YOLOv8 Detection
Human Body & Posture Assessment
• Toxic Gas Heatmapping
Multi-Gas Thresholding & Hazard Zones
4. RISK & GOVERNOR
“Assess Safety”
• Tunnel Hazard Index
Composite Score (Toxicity, Heat, Slopes)
• Drop-Off Proximity
Steep Slope & Water Hazard Avoidance
• Safety Governor
HARD CONSTRAINTS: Overrides AI Autonomy
• Emergency Rollback
Automatic Safe Retreat on Critical Gas
• Blackbox SD Buffer
Store-and-Forward Mission Flight Data
5. AUTONOMY & NAV
“Decide & Plan”
• Frontier Exploration
Autonomous Waypoints in Comms-Loss
• Risk-Aware A* / D*
Path Planning Avoiding High-Risk Pockets
• Bounded Autonomy
Time/Distance Limited Exploration Protocol
• Auto-Return Timer
Reverse Pathfinding to Signal Link
• Mission Scheduler
Energy & Battery Aware Navigation
6. ROVER ACTUATION
“Act & Deploy”
• 4WD Rugged Chassis
High-Torque DC Geared Motors
• BTS7960 Drivers
Dual H-Bridge Motor Control Modules
• Pan-Tilt Gimbal
2-Axis Servo Camera Surveying Head
• Breadcrumb Deployer
Wireless Mesh Relay Dispenser Mechanism
• Emergency Beacons
High-Lumen Strobe & Acoustic Buzzer
SURFACE RESCUE TEAM DASHBOARD & SITUATIONAL AWARENESS (Base Station Station / Control UI)
🗺️ Live 2D Tunnel Grid Map & Hazard Heatmap | 📹 Low-Latency Video + Thermal Overlay Feed | 📡 Breadcrumb Mesh Signal & Telemetry Link | 🚨 Survivor Markers & Timestamped Mission Log | 🕹️ Manual Override & Emergency E-Stop Controls
Guiding Principle: “AI Assists Detection — Rescue Team Makes the Final Decision” | Bounded Autonomy During Signal Blackout